Spectroscopy / Fluorescence

1. Review

A. Nature of light

Electromagnetic wave – moving electric and magnetic force field

E = h = hc/  (different names depending on energy or wavelength: for  in cm)

3000 (radio) / 0.3 (microwave) / 0.003 (IR) / 0.00003 (UV) / 0.00000003 (X-ray)

B. Effect of Light on Molecules -  vision / photosynthesis / radiation therapy

C. Effect of Molecules on “Light” –

Absorption / Fluorescence / X-ray / Light Scattering / CD / ORD / UV / NMR

Interaction of Light with Matter (induce oscillating dipoles in matter)

a) Scattered – 	(~ 10-16 sec )

Rayleigh scattering (s = i)   RG,  CD,  ORD

Raman scattering–  inelastic (s ( i)

b) Absorption - (~ 10-15 sec ) – due to “transition” from one energy level to another

Since absorption is fast relative to molecular motions

– insensitive to molecular motions

2. Absorption Spectrum – “fingerprint”

Beer-Lambert Law:   	Absorbance (A); Intensity (I, Io);  Transmittance (T = I / Io)

A = log (Io / I) = log (1/T)

Extinction Coefficient – E (1%),    = Molar extinction coeff.

A = O.D. =  (c(l       also     [  E1% (MW  =  10 ( M ]

Proteins:  		A280 ;  E (1%) ~ 10 (or O.D. of 1 for 1 mg/mL)

Nucleic Acids:	A260 ;  E (1%) ~ 200 (or O.D. of 1 for 50 g/mL)

3. Environmental Effects

nonpolar  >  polar  (folding / unfolding effect)

DNA – Helix-Coil Transitions (  free base  >  ss  >   ds  ) follow denaturation

4. Instrumentation

Light Source - Monochromator (filter, prism, grating) - Slit - Cuvette -Detector (PM tube)

5. Fluorescence  /  Phosphorescence

Fluorescence (~ 10-4 sec to 10-9 sec )   /   Phosphorescence  (> 10-3 sec )

Fluorescence signal is very sensitive to environment and molecular changes.

Instrumentation:  Measure fluorescence perpendicular to light path and at different 

very low background

Resonance Energy Transfer – needs “spectral overlap”

(Efficiency can be used to estimate distance from donor to acceptor.)

R = Ro[(1-)/]1/6  or  FRET (Fluor. Res. Energy Transfer) Eff.  =  1/[1 + (R/Ro)6]